## Slide 1: A typical LHC week
Coordination: Eva Barbara Holzer, Mike Lamont

## Slide 2: Sunday morning
07:40 Fill 2007 dumped – PIC PLC R1 UJ16
  Lost matching section R1
  Markus Zerlauth: memory corruption, remote reset possible
  Stable beams: 17h12m ~80 pb-1 delivered in Atlas/CMS
Reset, pre-cycle and go, but no…
PS RF low-level problems
  tuning of the 40MHZ cavity in the PS and then a RF low level problem - here be the dark wizards and black arts; dark wizards on holidays
17:45 Injecting physic beams

## Slide 3: Sunday evening
19:11 Stable beams #2008
  1.72e14
  ppb: 1.25e11
  initial lumi ~2.1e33
  lifetimes > 25 hours
  no apparent blow-up
19:38:54 Beams dumped – quench looped open – RQ4.R5, RQ10.R5, and RD2.R5
  It is not clear for the time being whether this was beam related (losses affecting QPS) or it was an EM disturbance.. UFO buster caught a small event in correspondence of the beam dump, which points to the first alternative – investigations ongoing.

## Slide 4: Last night
The VAC valves in IP5-R closed due to a vac spike at around 23:10.
  Valves closed at 19:38. This is clearly related to the beam dump.
  Pressure was increasing since ~18h. We checked: a similar increase occurred also during injection and ramp of the previous fill.
  The piquet reported also that he see temperature increase in region of D2-Q4.
  BIC history: the VAC interlock occurred 2.6 s after the beam dump. So the vac spike is not the direct source
SPS B2 kicker problems
02:48 Stable beams – fill 2009
  1.71e14
  Peak luminosity 2.1e33
  1.24e11 ppb

## Slide 5: Week 31: main timeouts
Monday 1st to 23:30 - cryogenics recovery
Thursday afternoon
  Access in shadow of POPS deployment
    PIC, BLM, QPS, Cryogenics, MKI point 2, Patrol lost – PM56…
Thursday evening
  Booster – slow kicker problem
  BPM in LSS6, spurious interlocks from BLS in LSS2
  Injection oscillations, re-steering B2
Sunday
  PS RF
1
2
3
4

## Slide 6: Last week: fills above 450 GeV
Start | Fill | Mode | Stable [h] | Int. L (pb-1) | Dump cause
Mon 1 | 1997 | STABLE | 2h46m | 17.0 | Cryo PLC point 1 (SEU?)
Tue 2 | 1998 | STABLE | 6h54m | 37.3 | RF
Tue 2 | 1999 | STABLE | 11h21m | 57.2 | Electrical network glitch (FMCM)
Wed 3 | 2000 | STABLE | 21h32m | 90.6 | OP dump
Thu 4 | 2001 | STABLE | 2h49m | 18.4 | PIC PLC point 5
Fri 5 | 2005 | STABLE | 22m | 2.0 | PIC PLC point 1
Fri 5 | 2006 | STABLE | 25h59m | 100.4 | OP dump
Sat 6 | 2007 | STABLE | 17h12m | 81.5 | PIC PLC R1
Sun 7 | 2008 | STABLE | 27m | 3.3 | D2.R5 quench loop
Mon 8 | 2009 | STABLE | … | 30+ | …
Bunch intensity gently pushed up to ~1.25e11
Average emittance ~2.0 microns

## Slide 7: 2006: Luminosity lifetime

## Slide 8: 2006 BCT

## Slide 9: Beam size (from Atlas lumi region)
~growth rate 64.4 hours
growth rate ~84.4 hours

## Slide 10: Beam lifetime >25 hours improving to ≈50 hours during the fill

## Slide 11: One batch blow-up with 1.25e11

## Slide 12: Vacuum on stepping up to 1.25e11 ppb
fill 2007

## Slide 13: Next fill - start 2008

## Slide 14: Losses on TCTVB.4R8
We have found that the losses at the TCTVB.4R8 are actually correlated with the losses at the TCP of IP3 - good correlation with the vacuum signal VGPB.656.5R3.R.PR

## Slide 15: Misc
Tunes increased by 1e-3 both beams, both planes
Bunch length SPS BQM frustrating injection
Cryogenics: automatic reset of PLCs point 1 deployed
Insulation Vacuum
  One of the 3 turbo pumps pumping the known helium leak in sector 3-4 (subsector A27L4.M) had failed on Sunday ~13:15.
  Monday: turbo pump replaced and vacuum pressure returned to the level prior to the failure.
MKI interventions (Mike Barnes)
  Ferrite installed on input triggers (G1, G2A and G2B triggers) to the thyratron trigger unit, of:
  Trigger Main 3, Trigger Dump 3, Trigger Main 4, Trigger Dump 4
  Note: following above some further runt trigger outputs were seen on MS3 G1 up until 13:00hrs. Returning after lunch, no more runt triggers occurred......
  Replaced the crate for G1 trigger units of M3, D3, M4 & D4

## Slide 16: Incoming
Loss maps
SPS magnet change
Test of squeeze to beta* = 1 m
Test of determinsistic satellite generation
PM56 to sort out defintively

## Slide 19: W31: records (c/o Atlas & CMS)