## Slide 1: Thu 02/08
12:09 dump by OP: 12.5 hours in stable beams; Integrated lumi: ~149 pb-1.
13:38-17:00 series of problems in sequence:
  SPS B2 extraction (BPM interlock)
  Vacuum interlock on LHC transverse damper (VB1 and HB2). Vacuum spike.
  PS main power supply down
17:00 Problem with QPS controller on RQD.A23 (33.L3). Access required.
19:36 End of access: power supply of the QPS detection unit replaced. In the shadow verification of the RQF.A12 energy extraction (following spurious opening on sunday night)

## Slide 2: Thu 02/08
19:44 Lost patrol in PM18 (door YCPS01=PM18). Already happened last friday. Piquet intervention to replace relay on the door
21:20 Patrol completed and machine closed - Precycling
22:30 injection finally.
Fill with equal settings for B1 and B2  reduction of damper gain by 25% for B1 H and reduction of the octupoles for B2 (~10 %)
00:22 Stable beams #2905 Initial luminosity 5.9x1033 cm-2s-1

## Slide 3
00:40 Beam dump due to trip of RQ5.L8 ~6 pb-1 in 20 mins. SEU ?

## Slide 4
03:43 Stable beams #2906. Initial luminosities 6x1033 cm-2s-1
04:38 beam dump due to UFO @ MKI2 (156% of dump threshold). 18 pb-1 in 55 mins

## Slide 5
06:28 Fill #2907. Dumped once more by UFO during the first part of the squeeze (100 %!!!)
Filling rather rocky with frequent IQC vetos.

## Slide 6: Beam quality
Still rather large emittances particularly B2V
Emittance increasing along the SPS trains

## Slide 7: Losses during the squeeze

## Slide 8: Plans
Fill for physics
Still pending: scraping of tails

## Slide 9: Pending
Change CTRV cards on TSU FECs for LBDS  N. Magnin (2 h)
Moving of the spare MKD generator from gallery to the surface