## Slide 1: Thursday morning
Waiting for LINAC, PS back on POPS, MKE4 intervention in the SPS.
LHC side:
  MKI2 faulty – heater module exchanged.
  Q7.R4 trip. Intervention in the tunnel. Cable segment replaced on DFB.
  CMS access for RPC.
13:00 Cycling.
  In the shadow fix of the BLM logging.
15:00 Injection.

## Slide 2: Thursday afternoon/night
16:30 Stable beams fill 2996, L ~7E33 cm-2s-1.
20:10 Dump due to electrical glitch – caught be FMCM on RD1.LR5. Integrated L 71 pb-1.
  Some issues with DIP affecting LHCb leveling (data delay).
21:00 Filling again.
22:45 Stable beams fill 2997, L ~7.2E33 cm-2s-1.
  Again ATLAS few % higher than CMS at the start of fill.
04:00 Beam dump, QPS on Q4.L1.
  Heaters fired, lost cryo.
05:00 TDI.4L2 stuck, interlock violated by 7 um.
  Intervention by A. Masi to unblock.

## Slide 3: Today
07:00 Refill starting…