## Slide 1: Tue 15/1
08:30 Power glitch (see F. Duval):
  PC trips in all sectors. Main circuits OK in S23, S34 and S45
  RF tripped
  ATLAS Solenoid and toriod tripped
  ALICE solenoid tripped
  Undulator RU.L4 quench
  Cryo P18 tripped
Source refurbishment launched
Accesses for:
  CV (US15)
  ALICE ZDC
  Closed ventilation in UJ32
  CMS

## Slide 2: Tue 15/1
Some issues with the publication of the CMS luminosity via DIP fixed during the afternoon.
Source back in operation at the end of the afternoon
20:30 problem with Beam Imminent Warning sirenes in point 5. Not possible to close the machine. Called expert.
Intermittent communication problems with the cryo in point 4 being investigated.
21:00 Cryo OK
22:16 Problem with TDI movement. EN/STI piquet called
23:30 Undulator trip (RU.L4). Lost matching section L4.

## Slide 3
00:03 TDI OK after several attempts from the piquet (??)
03:36: No way to repair the problem with the BIW sirens in P5. Forced the 'start cycle' locally; the rest of the signals followed nicely. Safety is ensured despite the repeated failures of returning the signals. To be followed-up this morning.
04:13 Injection of B1
04:14 lost cryo conditions in Sector 34/45 due to communication problem
06:30 Identified faulty network switch. Access to replace it (should start soon)
2-3 hours to recover if no cryo stop. Warned experts for BIW to fix problem during cryo recovery

## Slide 4
Loss maps at flat-top and LSS7 collimator alignment checks – go thorugh the squeeze off momentum and measure beta beating (6-8 hours)
IR2 aperture measurement (4 hours)
Ramp, cogging, frequency lock p/Pb (13 bunches) + TCT alignment and loss maps up to collision (>1 shift). In collision Roman pot alignment (TOTEM and ALFA vertical).
If problems to find collision inject nominal bunches and find collisions (4-6 hours) then go back to collimator alignment/loss maps
Injection of trains of 24 bunches (protons and ions) (2 hours)
Loss maps at injection (2 hours)
Remaining loss maps at flat top after generation of the functions (2 shifts)

## Slide 5: Validation
 | Injection (Inj. Prot. IN) | Injection (Inj. Prot. OUT) | Flat-top | Squeezed, separated | Squeezed Collision
Betatronic-H | tbd | tbd | tbd | tbd | tbd
Betatronic-V | tbd | tbd | tbd | tbd | tbd
Neg. off-mom | tbd | tbd | -- | tbd | tbd (+500 Hz)
Pos. off-mom | tbd | tbd | -- | -- | tbd (-500 Hz)
Asynch dump | -- | -- | -- | tbd | tbd
tbd=to be done