## Slide 1: Tuesday
08:40 Stable beams fill 3405.
  VdM IR 8, followed by VdM IR2.
  Length scale calibration IR1.
  End of fill just ‘normal’ stable beams.
15:40 Separated beams in IR1 and IR5 a (rather large) ‘bit’ to observed change of lifetime.
  Unfortunately beam dumped a couple minutes later.
  Small improvement in B2 lifetime.
15:50 Beam dump – standard BPM interlock.

## Slide 2: IR1/5 separated

## Slide 3: Tuesday
16:00 Access needed for QPS.
LHCb dipole polarity inversion.
A vertical bump of +1 mm was added to B2 for the BGI.
  Constant along the cycle.
Target bunch length at injection to 1.5 ns for ions.
17:30 Cycling.
19:00 Injection – back to standard schema.
20:40 Stable beams fill 3506.
03:50 Dump after 7:10 of stable beams by usual interlock BPMs. But rather good timing !!

## Slide 4: Wednesday morning
04:00 Problems to load some RF settings – piquet intervention required.
Temperature alarm in UX45 Faraday cage.
06:10 Injection.
07:00 RF re-synch needed.
  OFC reboot during a Q’ measurement messed up …
07:30 Access in UX45 for temperature alarm.
  Waiting for more informations to decide.

## Slide 5: Today and later…
Pb source refill  ‘afternoon’.
In the meantime:
  Stable beams, and /or
  ADT test on B2 in preparation for quench test, and /or,
  Access
Request from PS to try out a new extraction bump with the ions (already done with the p in December) and the protons.
  Make it depend on beam inversion timing.
Got 4 nb-1 with this polarity. ALICE wants >= 6 nb-1. We can make it for bam inversion on Friday.

## Slide 6: Beam reversal
Preparation: 8 hours
  Settings changes, ADT attenuators…
  TL steering,
  Checkout at injection (RF etc).
  Injection loss maps.
Cycle #1: 4 hours
  Check-out, cogging Pb-p and optics measurements.
Cycle #2: 8 hours
  Collide, TCT alignment, RP alignment, beta-loss map, asynch dump test in collisions.
Cycle #3: 3 hours
  Beta-loss map flat top, end of squeeze, off-p map in collision.
Cycle #4: 3 hours
  Missing beta-loss map, off-p map in collision.