## Slide 1: Status of energy calibration at LHC
J. Wenninger

## Slide 2: Proton-ion calibration principle
The difference in speed (or corresponding RF frequency) of protons and ions can be used to determine the momentum P of the beam:
LHC
~4.5 kHz
~20 Hz
At 4 TeV the effect is small and systematic errors dominate the measurement uncertainty
~59 Hz

## Slide 3: Cogging at 4 TeV
Proton and lead beam at flat top:
  Different RF frequencies for p and Pb,
  Both beams ~ centered.
Proton and lead beams after cogging:
  Same RF frequency for p and Pb, ~ average of p and Pb,
  Protons move to the outside, Lead ions to the inside.
x
x
Dx  Df

## Slide 4: Example : proton & lead orbits
Proton-Pb orbits at 4 Z TeV after cogging (at same RF frequency) revealing the revolution frequency difference  radial position offsets.
Protons – B1
Lead – B2
We are looking for an accuracy of ~ 10 mm on the radial position

## Slide 5: Measurement method
The frequency offset is deduced from the orbit offsets of the 2 beams – sensitive to the average BPM offsets wrt center of the LHC quadrupoles !
x
R1
R2
R1
R2
Dfmeas,A = Df + (d1 + d2)
Dfmeas,B = Df - (d1 + d2)
The systematic error from BPM offsets cancels out on the average of the measurements of p-Pb (A) and Pb-p (B) !
d1
d2

## Slide 6: Results - PRELIMINARY !!
Mean value p-Pb + Pb-b : 3.99 TeV ± (to be evaluated)
4 TeV
p-Pb
Pb-p
Mean value

## Slide 7: Systematics
Correlation Pb – p frequency – no anomaly.
  Changing values: tides etc
p-Pb
Pb-p

## Slide 8: To do
Collect more fills..
Systematic analysis of BPM scale and offset.
  Scale calibrations are all consistent:
    Can be checked in every fill during the cogging,
    Dedicated calibration (5 mins each).
  Offset dependence on bunch intensity, bunch length and time.
  Time: split the sample and look for significant changes etc…
  Intensity and bunch length:
    Could try to estimate it from the data itself.
    ~1 hour exercise at injection with scraping and RF voltage.