## Slide 1: LHC machine commissioning and the near future
Mike Lamont for the LHC team

## Slide 2: It’s been a long year…

## Slide 3: From diddly-squat…
> 4 orders of magnitude in 6 months
2e27
5e31
Bunch trains
Nominal bunch intensity

## Slide 4: Associated parameters
 | Present | Design
Energy [TeV] | 3.5 | 7
beta* [m] | 3.5,3.5,3.5,3.5 m | 0.55,10,0.55,10
Emittance [microns] | 2.5 – 3.5 start of fill | 3.75
Transverse beam size at IP [microns] | around 60 | 16.7
Bunch current | 1.1e11 | 1.15e11
Number of bunches | 152 140 collisions/IP | 2808
Stored energy [MJ] | 10 | 360
Peak luminosity [cm-2s-1] | 5e31 | 1e34

## Slide 5: Stored energy
Ralph Assmann

## Slide 6: Commissioning – Where do we stand?

## Slide 7: Operational Cycle
Injection
Ramp
Squeeze
Collisions
Ramp-down
Injection | Ramp | Squeeze | Collisions | Ramp-down
Multi-bunch, unsafe beam | Dynamic effects Feedbacks | Optics Collimators | Beam steering Beam-beam | Ramp rates Reproducibility
 All through the cycle 
Beam dump Collimations system Protection devices

## Slide 8: Injection
Now inject 16 nominal bunches per extraction from the SPS
  1.6e12 protons is above the safe beam limit at 450 GeV
  Careful adjustment of:
    transfer lines and collimators
    energy matching between SPS and LHC
    injection protection devices (transfer line collimators etc.)
  Transverse damper fully operational to damp injection oscillations
Transfer line collimator
Ring magnets with beam loss monitors

## Slide 9: Beam transfer and Injection

## Slide 10: Transverse dampers
OFF
ON
Crucial to keep emittance growth under control
Operational through the cycle – including stable beams
Turn number
Injection
Transverse position

## Slide 11: Ramp
450 GeV – 3500 GeV
  17 minutes
  Parabolic – exponential – linear – parabolic to minimize effects of snapback and duration
  Snapback correction pre-programmed for b2,b3,b4,b5,a2,a3 based on FIDEL predictions for full decay
Preloaded functions to power converters, collimators, RF
  ramp initiated with timing event
Fill-to-fill feed-forward performed intermittently
Tune and orbit feedback considered mandatory
  The performance of the FBs is good and the LHC only operates reliably with both orbit and tune FBs (ramp and squeeze).
Ramp and squeeze essentially without losses….

## Slide 12: Ramp – Tune feedback
Feedback employed early. Reconstructed tune excursions

## Slide 13: Feedbacks in action: ramp
OFB trims (mrad)
QFB trims
Energy (TeV)
Fill 1309
29.08.2010

## Slide 14: Orbit feedback performance: ramp
Orbit stability in the ramp: ≤ 80 mm rms
R. Steinhagen

## Slide 15: Beam current during fill 25/08/2010
“The price of freedom is eternal vigilance.”
Quite frankly: we’re dreaming…

## Slide 16: Squeeze: a delicate process
From 11-10-11-10 to 3.5-3.5-3.5-3.5 m
Move to collisions tunes at start
Tune and orbit feedback on
Worry about
  Tune, Q’, coupling, orbit, optics corrections
  Positions of tertiary collimators
Squeeze in three stages at the moment

## Slide 17: Beam intensities up the ramp…
Ramp
Bunch length
artifact
Squeeze
Collide
1%
B1
B2
Fill 1308
28.08.2010
…and through the squeeze
again essentially without loss

## Slide 18: Measured betas at interaction points

## Slide 19: Optics & magnetic machine
Optics stunningly stable
Machine magnetically and optically well understood
  Excellent agreement with model and machine
Magnetically reproducible
  Important because set-up remains valid from fill to fill

## Slide 20: Crossing angles

## Slide 21: Crossing angle – IP2
John Jowett

## Slide 22: MACHINE PROTECTION
Briefly, why we can’t deliver 1e32 cm-2s-1 immediately

## Slide 23: Quench Limit of LHC Super-Conducting Magnets
Beam
10 MJ
SC Coil:
quench limit
15-100 mJ/cm3
56 mm
Situation at 3.5 TeV (in October 2010)
Not a single beam-induced quench at 3.5 TeV … YET

## Slide 24: Beam Interlock System & Beam dump
IR6 H Beam2, extracted
Beam interlock system
  Tells beam dump to fire with 3 turns
  Around 20,000 inputs
  Caught everything so far
Beam dump system (LBDS)
  Well set-up and closely monitored
  No major issues yet

## Slide 25: Abort Gap
dump trigger
3.0 ms
particle-free
abort gap
Extraction kicker MKD deflection
LHC
Beam

## Slide 26: Asynchronous Beam Dump
TCSG
TCDQ = 6 m long CFC* one-sided collimator TCSG = 1 m long CFC* two-sided collimator
TCDQ + TCSG to protect downstream superconducting magnets (Q4)
*CFC = carbon fibre compound
Estimated occurrence : at least once per year,
0 events up to now!

## Slide 27: Beam dump protection systems efficiency
1e-3 leakage to tertiary collimators in IR’s
 OK for stable beams from beam dump
Provoked asynchronous beam dump

## Slide 28: Collimation system

## Slide 29: Ramp - collimators

## Slide 30: Collimation set-up
Collimation is set up with multi-stage logic for cleaning and protection
In normalized phase space, talking in nominal sigmas:
Primary
Secondary
Dump Protection
Tertiary
+Triplet
Tertiary
+Triplet
Dump Kicker
Beam dump envelope
ROBUST
Not robust
Not robust
… but efficient …
MARGIN
“THE HIERARCHY”

## Slide 31: Measured Cleaning at 3.5 TeV
IR8
IR1
IR2
IR5
Momentum Cleaning
Dump Protection Col.
(beam1, vertical beam loss, intermediate settings)
Making sure the hierarchy is respected

## Slide 32: Zoom around betatron cleaning
 OK for stable beams from collimation
factor 1,000
factor 4,000
IR8
factor 600,000

## Slide 33: Why we spend so long messing around…
The collimators and protection devices must be in position at all times
The hierarchy must be respected
The collimators and protection devices are positioned with respect to the closed orbit
Therefore the closed orbit must be in tolerance at all times. This includes the ramp and squeeze.
  Orbit feedback becomes mandatory
  Interlocks on orbit position become mandatory
If these rules are not respected something will get broken.
Frequent validation to make sure that the rules are respected…
Full validation with new set-ups – takes time

## Slide 34: Measured 450 GeV Aperture
On-momentum, as relevant for collimation and protection.
Predicted aperture bottlenecks in triplets (n1=7) are less than expected (orbit, alignment, mechanical tolerances)
“Measured” n1 = 10 – 12 (on-momentum) instead of the design value of n1 = 7. Excellent news…
Beam / plane | Limiting element | Aperture [s]
Beam 1 H | Q6.R2 | 12.5
Beam 1 V | Q4.L6 | 13.5
Beam 2 H | Q5.R6 | 14.0
Beam 2 V | Q4.R6 | 13.0

## Slide 35: LUMINOSITY PRODUCTION

## Slide 36: Luminosity
Very good single beam lifetime
  Inject nominal bunch intensities, ramp, squeeze…
  Vacuum, non-linearities, IBS, noise
Beam-beam (head-on)
  Nominal bunch intensity
  Less than nominal emittances
  A lot easier than expected – nominal figures exceeded
  Resolved expected problems with predicted cures.
    Octupoles, transverse dampers cope with instabilities
Transverse emittance (read beam size)
  Too small emittance from injectors! Blow-up required.
  Ditto longitudinal plane
Luminosity lifetime
  Of the order 20-25 hours
  Single beam, luminosity, emittance growth
STILL SURPRISING

## Slide 37: Collisions – emittance blow up
calculated with measured bunch intensity, nominal ge = 3.75 mm and b*=3.5m
Emittance growth
ATLAS
CMS
CALCULATED
Machine parameters very well controlled!

## Slide 38: Coupled with remarkable machine availability
Impressive performance of:
  cryogenics,
  QPS
  power converters
  RF
  instrumentation,
  collimators,
  vacuum,
  beam dump and kickers,
  services,
  Injectors, …
Hard work of the many teams to constantly improve weaknesses and to keep it all working.
Courtesy ATLAS
Time in Stable Beams
= integrated luminosity

## Slide 39: Two weeks in August
48b
50b
25b

## Slide 40: Luminosity scans
Simon White
Luminosity calibrated with van der Meer scans
Luminosity known today to around 11% - error dominated by current measurement
Dedicated campaign underway

## Slide 41: PROBLEMS, PROBLEMS

## Slide 42: The hump - source still unknown
External excitation
Tunes

## Slide 43: Tune signal swamped in the ramp
With increasing intensity/number of bunches
NOT good for tune feedback

## Slide 44: Vacuum – from yesterday
Inner Triplet left 1 (VGPB.7.4L1.X):
  Start pressure before filling: 1.8x10-10mbar
  End pressure after filling: 4.3x10-8mbar
Possibly HOM induced cleaning…

## Slide 45: SEUs
SEU count (RADMON) during off momentum loss map
QPS crate
Thijs Wijnands
Not a problem at the moment but being monitored carefully

## Slide 46: UFOs – sudden local losses
12 events of sudden local losses (some in the middle of the arc) have been recorded. No quench, but preventive dumps
Rise time partly < 1 ms.
Potential explanation: dust particles falling into beam creating scatter losses and showers propagating downstream

## Slide 47: 2010 incoming

## Slide 48: Schedule – rest of 2010
104
152
200
240
288
336
Reserve!
Number of bunches | Peak Luminosity [cm-2s-1] | 5day@0.2HF [pb-1] | MJ
336 | 1.0 x 1032 | 8.9 | 20.7
Next up: 150ns_200b_186_8_186_8+8bpi17inj

## Slide 49: Early Heavy Ion Run
 |  | Early (2010/11) | Nominal
√s per nucleon | TeV | 2.76 | 5.5
Initial Luminosity (L0) | cm-2s-1 | 1.25 x 1025 | 1027
Number of bunches |  | 62 | 592
Bunch spacing | ns | 1350 | 99.8
b* | m | 2 | 0.5
Pb ions/bunch |  | 7x107 | 7x107
Transverse norm. emittance | mm | 1.5 | 1.5
Luminosity half life (1,2,3 expts.) | h | tIBS=7-30 | 8, 4.5, 3
Initial interaction rate: 100 Hz (10 Hz central collisions b = 0 – 5 fm)
~108 interaction/106s (~1 month)
In two years: 2 x107 central collisions, integrated luminosity 25 mb-1

## Slide 50: 2011 – 3.5 TeV
Restart 4th February (?)
9 months protons, 4 weeks ions
Integrated luminosity target driven: 1 fb-1
Need to run flat out above 1e32 cm-2s-1
Beta* etc. under close examination – tests incoming

## Slide 51: Conclusions 1/2
Injection, ramp and squeeze operational
LHC magnetic model, optics astoundingly good.
Beam instrumentation in good shape.
Feedbacks on orbit and tune(?) operational
Beam cleaning and collimation works reliably with predicted efficiency.
Machine protection reliably catches failures etc.
Machine aperture looks very good
Remarkably few problems colliding nominal bunch intensities

## Slide 52: Conclusions 2/2
All key systems performing remarkably well & there are some hugely complex systems out there.
  Some commissioning still required, issues still to address
  And NB there are still problems
Handling dangerous beams already - have to remain vigilant at all times (and not get carried away)
Performance with beam (losses, lifetimes, luminosity, emittance growth etc.) is very encouraging
Machine availability is excellent – the hard work of numerous teams
On route towards 1032 cm-2 s-1 for end of the year - a factor 2 to go