## Slide 1: Status of the LHC
Mike Lamont for the LHC team

## Slide 2: The LHC
Very big
Very cold
Very high energy

## Slide 3: Energy
~3 GJ of energy stored in the magnets
100 MJ stored in each beam ~21 kg of TNT.
Underpins our thoughts
3.5 TeV with 1380 bunches – September 2011
During an SPS extraction test in 2004…
The beam was a 450 GeV full LHC injection batch of 3.4 1013 p+ in 288 bunches [2.5 MJ]

## Slide 4
2008
2009
2010
2011
LHC Timeline
September 10, 2008
First beams around
September 19, 2008
Disaster Accidental release of 600 MJ stored in one sector of LHC dipole magnets
November 29, 2009
Beam back
August 2008
First injection test
August, 2011
2.3e33, 2.6 fb-1
1380 bunches
October 14 2010
1e32
248 bunches
November 2010
Ions
March 30, 2010
First collisions at 3.5 TeV
1380
June 28 2011
1380 bunches

## Slide 5
February
March
April
November
October
May
June
July
August
September
March 30
First collisions 3.5 TeV
A closer look at 2010
April
Commission squeeze
Feb 27
Beam back
June
Commission nominal bunch intensity
QUALIFICATION
September
Crossing angles on
October
Luminosity production

## Slide 6: 2010 – integrated luminosity
EXPLOITATION
COMMISSIONING
and frantic debugging
CONSOLIDATION

## Slide 7: Nominal cycle
Beam dump
Ramp down/precycle
Injection
Ramp
Squeeze
Collide
Stable beams
Ramp down | 35 mins
Injection | ~30 mins
Ramp | 17 mins
Squeeze | 8 mins
Collide | 1 mins
Stable beams | 0 – 30 hours
Fastest turn around down from 3h40m in 2010 to 2h7m in 2011 after optimization

## Slide 8: Aperture
Aperture systematically measured (locally and globally)
Better than anticipated w.r.t. tolerances on orbit & alignment
Aperture compatible with a well-aligned machine, a well centred orbit and close to design mechanical aperture

## Slide 9: Optics
Optics stunningly stable
and well corrected
Two measurements of beating at 3.5 m 3 months apart
Local and global correction at 1.5 m

## Slide 10: Magnet model
Model based feed-forward reduces chromaticity swing from 80 to less than 10 units
Knowledge of the magnetic machine is remarkable
All magnet ‘transfer functions’, all harmonics including decay and snapback of persistent currents
Tunes, momentum, optics remarkably close to the model

## Slide 11: Reproducibility
Tune corrections made by feedback during squeeze
7 e-3
LHC magnetically reproducible with rigorous pre-cycling - set-up remains valid from month to month

## Slide 12: Machine protection – the challenge
Beam
100 MJ
SC Coil:
quench limit
15-100 mJ/cm3
56 mm
Situation at 3.5 TeV (in August 2011)
Not a single beam-induced quench at 3.5 TeV … YET
11 magnet quench at 450 GeV – injection kicker flash-over

## Slide 13: Beam Interlock System
Beam Interlock System
Beam
Dumping System
Injection Interlock
Powering
Interlocks
superconducting magnets
Powering
Interlocks
normal conducting magnets
Magnet protection system
(20000 channels)
Power
Converters
~1600
AUG
UPS
Power Converters
Magnets
Fast Magnet Current
change Monitor
Cryogenics
some 10000 channels
RF
System
(f_RF + P)
Vacuum
System
Beam Loss
Monitors
BCM
Collimation
System
Jaw Position
Temperature
Screens and Mirrors
beam observation
LHC
Experiments
BPMs
Beam loss monitors
BLM
Special BLMs
Monitors
aperture limits
(some 100)
Monitors in arcs
(several 1000)
Timing System
(Post Mortem Trigger)
Operator Buttons
CCC
Safe
LHC
Parameter
Software
Interlock
System
Safe Beam Parameter Distribution
Safe
Beam
Flag
Access
System

## Slide 14: Beam Dump System (LBDS)
Expected about two asynchronous dumps per year – one to date with beam
Absolutely critical. Rigorous and extensive program of commissioning and tests with beam.
IR6 H Beam2, extracted

## Slide 15: Collimation
beam
1.2 m
Two warm cleaning insertions IR3: Momentum cleaning 1 primary (H) 4 secondary (H,S) 4 shower abs. (H,V) IR7: Betatron cleaning 3 primary (H,V,S) 11 secondary (H,V,S) 5 shower abs. (H,V)
Local IP cleaning: 8 tertiary coll.
Total = 108 collimators
About 500 degrees of freedom.

## Slide 16: Collimation
Triplet aperture must be protected by tertiary collimators (TCTs)
TCTs must be shadowed by dump protection (not robust)
Dump protection must be outside primary and secondary collimators
Hierarchy must be satisfied even if orbit and optics drift after setup
  margins needed between collimators

## Slide 17: Collimation cleaning at 3.5 TeV
Generate higher loss rates: beam across the 3rd order resonance.
Betatron
Off-momentum
Dump
TCTs
TCTs
TCTs
TCTs
Beam 1
Legend:
Collimators
Cold losses
Warm losses
0.00001
0.000001
Outstanding performance: No beam-induced quenches in 2010/2011

## Slide 18: Exit 2010: beam parameters
 | 2010 | Nominal
Energy [TeV] | 3.5 | 7
beta* [m] | 3.5, 3.5, 3.5, 3.5 m | 0.55, 10, 0.55, 10
Emittance [microns] | 2.0 – 3.5 start of fill | 3.75
Bunch intensity | 1.2e11 | 1.15e11
Number of bunches | 368 348 collisions/IP | 2808
Stored energy [MJ] | 28 | 360
Peak luminosity [cm-2s-1] | 2e32 | 1e34

## Slide 19: Lead ion run 2010
Collisions within 54 hours of first injection
Experience and Lorentz’s law.

## Slide 20
2.6 fb-1
90 pb-1/day

## Slide 21: Emittance
As we move around the machine the shape of the phase space ellipse will change as (s) changes with the varying quadrupole (de-)focusing
However the area of the ellipse () does not change
Emittance shrinks naturally as we go up in energy (pS increases, pT doesn’t)
Define energy independent normalized emittance:
Units are mm.mrad but normally use microns (and drop ‘normalized’)
Useful – constant across complex (give or take some blow-up)
x’
x

x

## Slide 22: Aim: maximize peak luminosity
N | Number of particles per bunch
Kb | Number of bunches
f | Revolution frequency
 | Beam size at interaction point
F | Reduction factor due to crossing angle
 | Emittance
 | Normalized emittance
 | Beta function at IP

## Slide 23: Beam from injectors
Excellent performance
Higher than nominal bunch intensity Smaller than nominal emittance
Bunch spacing | From Booster | Np/bunch | Emittance H&V [mm.mrad]
150 | Single batch | 1.1 x 1011 | 1.6
75 | Single batch | 1.2 x 1011 | 2.0
50 | Single batch | 1.45 x 1011 | 3.5
50 | Double batch | 1.6 x 1011 | 2.0
25 | Double batch | 1.2 x 1011 | 2.7
At present: ~1.3 x 1011ppb, 2.0 microns into collision

## Slide 24
MD, technical stop
MD, technical stop
Intermediate energy run, technical stop, scrubbing
75 ns
50 ns
Smaller emittance
from injectors
MD, technical stop, SQUEEZE
2011

## Slide 25: 2011: (c/o Atlas & LHCb)
Peak stable luminosity | 3.29 x 1033 cm-2s-1
Max. luminosity in one fill | 114 pb-1
Max. luminosity delivered in 7 days | 499.45 pb-1
Longest time in stable beams | 26.0 hours
Longest time in stable beams for 7 days | 107.1 hours (63.7%)
Fastest turnaround | 2 hours 7 minutes
33% of design luminosity: - half design energy - nominal bunch intensity+ - ~half nominal emittance - beta* = 1.0 m (design 0.55 m)
- half nominal number of bunches

## Slide 26: Fill 2006: Luminosity lifetime
H growth rate ~64 hours
V growth rate ~84 hours
Lifetime beam 2
A “typical” fill that lasted 26 hours and delivered 100 pb-1
Luminosity lifetime
30 hours
Lifetime beam 1
100 hours

## Slide 27: 2011 parameters – now
Energy [TeV] | 3.5
Beta* [m] | 1.0, 10, 1.0, 3.0 m
Normalized emittance [microns] | ~2.0+ start of fill
Bunch intensity | 1.3e11
Number of bunches | 1380 1318 collisions/IP1&5
Bunch spacing [ns] | 50
Stored energy [MJ] | 90 to 100
Peak luminosity [cm-2s-1] | 3.3e33
Beam-beam tune shift (start fill) | ~0.023

## Slide 28: Availability - efficiency
Premature end to fills

## Slide 29: UFOs in the LHC
Since July 2010, 35 fast loss events led to a beam dump.
18 in 2010, 17 in 2011. 13 around MKIs. 6 dumps by experiments. 1 at 450 GeV.
Typical characteristics:
  Loss duration: about 10 turns
  Often unconventional loss locations (e.g. in the arc)
The events are believed to be due to (Unidentified) Falling Objects (UFOs).
Spatial and temporal loss profile of UFO on 23.08.2010

## Slide 30: Single Event Effects
Major campaign ongoing: shield and relocate

## Slide 31: Dumps > 450 GeV July-August
Room for improvement

## Slide 32: Availability 2011
Beam in ~49% of the time

## Slide 33: Rest of this year

## Slide 34: Rest of this year
3 fb-1 plus…
…another ~40 days and reasonable efficiency: might just manage another 2 fb-1
3.3 e33 cm-2s-1

## Slide 35
 | Days
Commissioning | 23
MD | 22
Technical stops | 20
Recovery & ramp-up | 16
Initial ramp-up | 16
Proton running | ~130
Special runs | ~8
Ion setup | 4
Ion run | 24
2012
Possible energy increase?
50 ns versus 25 ns?
DRAFT!

## Slide 36: Pile-up
Luminosity per crossing
Inelastic cross section (~72 mb at 3.5 TeV)
average number of visible interactions per bunch crossing

## Slide 37: Pileup
Bunch spacing | No. of bunches | Energy [TeV] | Beta* [m] | Normalized emittance [micron] | Protons per bunch [e11] | Peak lumi [cm-2s-1] | Peak mean mu
50 ns | 1380 | 3.5 | 1.0 | 2.0 | 1.3 | 3.37 | 16.4
50 ns | 1380 | 3.5 | 1.0 | 2.3 | 1.6 | 4.49 | 21.8
50 ns | 1380 | 4.0 | 0.8 | 2.0 | 1.3 | 4.1 | 19.9
50 ns | 1380 | 4.0 | 0.8 | 2.3 | 1.6 | 6.2 | 30.2
25 ns | 2760 | 3.5 | 1.0 | 2.8 | 1.2 | 4.1 | 10.0
25 ns | 2760 | 4.0 | 1.0 | 2.8 | 1.2 | 4.6 | 11.2
130 days at reasonable efficiency – might hope to push towards 10 fb-1

## Slide 38: Further ahead
NB: not yet approved

## Slide 39: Conclusion
Successful commissioning and good transition from commissioning to operations
  Cycle is solid
  Performance is quite staggering (and will now flatten out)
  Machine protection working well
  Availability with high intensity acceptable with issues being addressed
The LHC is a beautiful machine and a real testament to those who conceived, built and installed it.