## Slide 1: Day 23.3.
8:45 pre-cycle all sectors
  10am: trip of sector 78 (Cryo loss left of IP8)  need to pre-cycle again MS
11:30: end of pre-cycle in S78; beams back in LHC
  beam adjustments (tune, orbit, Q’)
  minor problems loading ramp table (QTD and QTF settings)
13:30: start ramp
  left accidentally TDI and TCLIs in during ramp. Still very good lifetime (70h to 100h) and no losses during ramp
14:30: end of ramp  measurement of orbit, Q and Q’
  orbit correction and IP steering & collapse of separation bumps
15:30: Start of collimation setup at 3.5 TeV

## Slide 2: 23.3.
Orbit at 3.5 TeV: difference between 450 GeV and 3.5 TeV
  Beam separation on

## Slide 3: 23.3.
Orbit at 3.5 TeV: IR steering
  IR5

## Slide 4: 23.3.
Collimation setup at 3.5 TeV
  Intermediate collimation setup summary (2.5h of beam at 3.5 TeV): - Golden orbit defined before collimation setup. - Emittance lower than nominal. - Had to close primary collimators to 4-5 nominal sigma (2mm) to see halo and define a halo edge. - Beam 1: 10 collimators out of 37 set up for 3.5 TeV beam. - Beam 2: 5 collimators out of 37 set up for 3.5 TeV beam.

## Slide 5: 23.3
Collimation setup at 3.5 TeV
  smaller than nominal beam sizes

## Slide 6: 23.3.
18:20 Beam dumped by ATLAS BCM
  pre-cycle machine to prepare for new fill
  machine BLMs only small minuscule losses (< 1% quench level thres.)
20:00: ready for beam
  beam adjustments (tune, orbit, Q’)
  wire scans & beta beat measurements
20:30: start LBDS setup at 450 GeV
  Beam2 injected into wrong bucket: Piquet suspects timing system
  re-synchronization with SPS solves the problem
  some problems with ‘inject & dump’ mode at around midnight
  injection of 10 bunches
  beam dump at intermediate energy: 2 TeV

## Slide 7: Night 23.3.
Summary LBDS studies:
  14 out of 15 MKD kickers checked for B1 and B2
  Beam centering in extraction channel checked for B1 and B2
  Extraction with 15 MKD corrector knob not clean - to be checked
  Measured beta functions at P6 elements - H betas at TCDQ for B1 are significantly larger than for B2.
  Interlock BPMs in P6 set to +/-3.6 mm around golden orbit for B1 and B2. Should be recheck for higher bunch intensity.
  Injected 10 bunches into B1 and B2 for total intensity of about 2-3e10 per beam, to check MKB kicker sweep. Both beam lifetimes very good.
  Dumped both multibunch beams with operator switch to get PM data. Beams dumped with no detectable losses in the ring or in the dump lines. Sweep pattern looks good.
  Beam dump at intermediate energy: 2 TeV

## Slide 8: 23.3.
Beam2 RF bucket:

## Slide 9: 23.3.
Wire scanner Beam2:
                H = 1.5
                V = 1.0

## Slide 10: 23.3.
Beta-beat Beam1:

## Slide 11: 23.3.
Injection of 10 bunches: Beam lifetime 100 hours!

## Slide 12: 23.3.
Beam on dump:

## Slide 13: 23.3.
Beam on dump at 2 TeV:

## Slide 14: 23.3.
21:00: In parallel to LBDS studies RF adjustments
  Problem with RF cogging for Beam2
  requires intervention in SR4
04:30: start ramp for 2 TeV dump
05:50: ramp down

## Slide 15: 24.3.
Tentative program:
  Ramp to 3.5 TeV
  Orbit and optics measurements
  Collimation check and set up at 3.5 TeV
  LBDS set-up (at 3.5 TeV)
Still not finished:
  RF tuning
  feedback studies
  damper studies

## Slide 16: 24.3.
Open Issues:
  Klystron in Pt4
  BI needs access for synchrotron light monitor
  RCBH22L2 B2 still requires intervention for PC communication
  RCBH19.L3B2, RCBV19.L3B1 (problem with the cryo-valve control)
  instability of the QPS controllers for RQT12.L5B1,RQTL11.L5B1/B2