## Slide 1: Monday 19th April 2010
8:30 end ramp
  orbit feedback on both planes
9:59 having squoozen to 5 m
  Dump B2: internal trigger of the LBDS
  Access required
Instead of beam dump we perform a short scraping test in IR7.
  First TCLA collimator TCLA.A6R7.B1 for beam1 moved into the beam. Recorded loss maps will allow to adjust TCLA thresholds more accurately.
  Beam dump triggered by BLM RS 655ms TCT collimator (TCTH.4L1) in IR1
Afternoon: access, pre-cycle, injection
Main quads in SIS
SIS Orbit timeout increase to 1 hour

## Slide 2: RT corrections at 3.5 TeV

## Slide 3: Orbit in ramp
Ralph Steinhagen owes me loads of beer for using more than a shift to commission OFB system

## Slide 4: TCLA BLM calibration

## Slide 5: Monday
17:30 start ramp
19:05 Start squeeze
  moderate beam loses
21:30 Both beam dumped
23:30 Back at injection
  SPS is shaky tonight, the mains went down once more. Also the PSB kicker has not been doing too well all day.
  The optics retrieval from LSA by the orbit feedback service unit seems to be broken and stalled after requesting a 'fetching optics'. The process FesaShared_M went to 100% CPU load and subsequently blocked the feedback controller resulting in transient or no orbit data. Restart of the OFSU server alone or unrolling to the old version did not help. Finally resetting (/deletion) of OFSU persistent data (left a copy in ../data/savea) seemed to help the situation. To be further investigated.... On top of this (later): after rebooting the OFSU overrode all Q/Q' FB gains and matrices to zero... sigh... re-established them by hand. As collateral, the radial trim (Q' meas) may need to be reset/reconfigured as well...

## Slide 6: Overnight
  .. finally had to bootstrap the whole Tune-FB from scratch... now OK.....
  next problem: continuous FFT systems are down and need to be restarted... sigh.
2:30 ramp started
2:33 Sector 78 tripped - beam dumped at 510 GeV
  RQF was the first to go,
  Likely reason of the beam dump of 2 30: a noisy splice signal
Recovery
07:00 Maskable and unmaskable BLM's in L2 are red and this prevents injection
  BIS (Bruno Puccio) and BLM (Bernd Dehning) in action

## Slide 7
Beam 1 unperturbed tunes seems to touch/cross due to large coupling and is eventually pushed across the 1/3 order resonance with moderate losses

## Slide 8: QPS – noisy splice signal

## Slide 9: Squueze

## Slide 10: Squeeze functions

## Slide 12: Plus

## Slide 13: Program for the week