## Slide 1: End-of-fill test separated collisions
Test of separated collisions in ALICE
  09:00-10:30 3 May 2010, ADJUST, 450 GeV
  2 x 2 bunches, Nb ~ 0.8 × 1011
  Emittance: Beam 1~nominal, Beam 2 ~ twice nominal
  Beams colliding in IP1, IP5, IP8
  Re-separated horizontally in IP2 to ±2 mm
  Separation scanned from +2 to -0.5 mm, few minutes each point
  No significant effects on emittance, lifetime or losses
Encouraging for high energy operation with luminosity reduced in ALICE