## Slide 1: Saturday 22.05
Stable beams from night
11:30 : PC trip RQTD.A81B2, water problem
  Access to repair.
  RSD2.A23B1 trip during access, requires additional access.
  Trip of RD1.LR5, electrical network perturbation.
19:30 : trip of RF, electrical network perturbation.
20:00 : Access finished
21:40 : injection
  B2 emittance increasing rapidly.
  Re-injected B2 with (almost) ‘everything’ ready to ramp to minimize emittance growth.

## Slide 2: Saturday 22.05
23:30 : Ramp
  Good news : we survived an ‘energy glitch’ event in the FB.
  Bad news : the FB does not manage to get back to normal state after the glitch. Enters an endless loop and thinks it is at 1 GeV. All values (kicks, Q corrections) published by the FB are ‘corrupted’. It still manages to correct (respectively not to loose the beam).
  >> We will have to reboot the server during every pre-cycle to reset the energy (unless we get a ‘far East’ patch…).
00:15 : Flat top
  Huge emittances:
  B1 4.5 um (H), 7.1 (V) B2 4.5 um (H), 6.4 (V)
  Problems to measure Q’ due to the issue with the energy (see above). With 1 GeV, the sign of dp/p changes wrt dfRF and Q’ comes out with the wrong sign !!
  Lost B2 while trying to understand Q’ (beam excursion interlock after intensity loss).

## Slide 3: Sunday 23.05
01:30 Ramp down
  Reboot FB did gave other issues.
  >> Decided not to use OFB for next ramp
06:00 Stable beams at last !