## Slide 1: From yesterday

## Slide 2: Wednesday 26th
Welcome Verena back on shift
07:08 Access in PM85 for piquet EPC (O.Fournier).
  Fuse on RD2.R8 circuit.
10: 20 RD2.R8 now ok. prepare to recycle.
14:00 Injecting 1 e11
  coherent instability induced by hump
15:00 ramping 2 * 1e11 for OFB test
  emittances already reasonably big starting the ramp
  B1H 4.6 B1V 6.5 B2H 7.5 B2V 6.9
  OFB looks good
15:39 Beam 2 lost to vacuum interlock

## Slide 3: Hump again

## Slide 4: BGI
BGI (Beam Gas Ionization) monitor was being tested, and after injection of 3 different level of gas, the BGI started to create discharges and the resulting out gassing gave vacuum gauge readings that were at the 10-7mb.
As the vac gauge readings were increasing, the two gauges closest to the BGI were masked by the vac expert.
The masking then caused an interlock on the vacuum system and the beam was dumped. Only after the beam dumped did a valve close.

## Slide 5: Orbit Feedback
Summary of the ramp with orbit FB: - No more dancing beams,this improvement seems to come from the RST period that was changed to 80 ms (from 100) to be in phase with the FB. - The FB survived an event without energy (due to the fact that the tune systems stopped for some time). It took some time to catch up the energy, but it eventually managed.
Declare operational with some potential tuning to be performed

## Slide 6: New Rest Gas Monitor: mechanical design The tank within its magnet
200 mm
F=84 mm
Light signal
cross section view
3-D view
Light signal
680 mm
e- signal
side view

## Slide 7: Big nominal bunches up the ramp
chromaticity difficult to measure
Colliding high intensity bunches in ATLAS and CMS. Looks stable. See about expected luminosity.
Bunch currents: 9.8e10 and 8e10.
Emittances 7-12 micron normalized.
Went to collision tunes.
Put an extra +3e-3 on beam 2 H and V (for tune split).
Stable after going into collision, rocky before collision with some manual chroma and tune trims to keep the beam.
First collided in CMS, optimized CMS, then collided ATLAS and optimized.
One round of optimization in beam-beam offset for each ATLAS and CMS.

## Slide 8: Nominal bunch intensity - synthesis
Over-injection well established
Emittance blow-up of beam 2 V at 450 GeV well documented
Emittance blow-up during ramp
Transverse instability at 1.8 TeV+
  cured by octupoles
Longitudinal
  longitudinal emittance at the SPS should be set at 1.7-1.8eVs
  plus matched voltage
Collisions at 10 m. looks OK with tune split and collision tunes

## Slide 9: First “nominal” collisions at 7 TeV

## Slide 10: Tune spectra 3.5 TeV

## Slide 11: Longitudinal “instability”…

## Slide 12: with 12 MV at 3.5 TeV

## Slide 13: Wednesday - Thursday
21:51 beams lost – mains glitch
20:03 RB in S67 tripped when doing the ramp-down
  trip of the RQF/QD caused by the nQPS where threshold is exceeded on B15L7. B15L7 signal crosses the 500 uV threshold due to a sinewave with a period of about 25 sec.
midnight - re-inject
00:34 lose S67 again – access required
  Switched board on RQTD.A67B1.
07:12 Pre-cycle finished
BLM crate HC.BLM.SR3.L problem between hardware card and CPU. No communication. No beam permit from this crate until fixed. Christos will go to point 3. Front-ends on the surface.

## Slide 14: Plans for today – to be discussed