## Slide 1: Tuesday 24/5
02:00 Stable beam fill #1804 912 bunches
  Initial lumi 1x1033 cm-2s-1
12:20 beam dumped fill #1804
  RF interlock beam 1, initiated by UFO point 4
  Integrated luminosity 29 pb-1
Access – “planned for one hour”
  Transverse damper amplifier, increase RF arc detection threshold and quench resistors cooling
17:30 Loss maps with injection protection in
Fill #1805
  18:30 Start injection
    Some problems with BPM calibration, injection losses & blow-up
  23:25 Stable Beams
  Initial lumi 1x1033 cm-2s-1
  02:43 Beam dump, RF cfv-sr4-allfo1 power supply down
Fill # 1806
  08:20 Stable beams, Initial lumi 1x1033 cm-2s-1

## Slide 2: UFO point 4
Dumped by RF arc detection – following a UFO in point 4
XPOC TCT.4L5.B1
PM TCTV.4L5.B1

## Slide 3: Loss Maps at injection
B1 – V:
With injection protection in, to check ratio TDI / TCP
B2 – V:
TDI
TDI
TCP
TCP
Looks OK

## Slide 4: Injection
Injection oscillations and losses for B1
  OK after trajectory correction
First, Beams blown up at injection as well
  OK for final injection

## Slide 5: Fill # 1805: 23:25 Stable Beams
02:43 cfv-sr4-allfo1 power supply down -> RF clock down Missing RF-frequency for beam dump: LBDS triggers as it should RF LL piquet changed the crate – no CO-FE first line
Going into physics now

## Slide 6: Injection kickers MKI Point 8 vacuum
Vacuum increase during end of filling stopping injection for a few minutes
Most likely e-cloud of interconnects between the injection kickers
Vac reading MKI-C stopping injection

## Slide 7: Injection kicker MKI warming up by the beam
Injection interlock set to 55 C measured magnet temperature
After checks this interlock level can most likely be increased until Curie temperature of magnet ferrite has been found
  Above Tcurie (around 120 C) kicker magnet will loose strength rapidly
  Difficult to perform reliable temperature measurement of ferrite which is under HV. Measured temperature ≠ Ferrite temperature.
25 C
45 C

## Slide 8: Plan
Wednesday
  Fill #1806 going into physics right now
  End of fill: RF tests switching off one cavity
  Test of RF power interlock
  TCLIB alignment
Thursday
  Physics
  End of fill: TCL adjustment
  Asynch dump test @ 3.5 TeV for Roman Pots
    Measure chromaticity for FIDEL over the ramp
Fri – Sun
  Physics