## Slide 1: Tuesday morning
08:30-09:00 Squeeze with probe.
  Very nice and stable orbit – only one ‘spiky’ excursion in the fist part of the squeeze. New parabolic rounding of correctors involved in Xing and separation bumps seems to pay off.
  Small RT corrections after a few iterations of feed-forward (each at the level of ~60%).
Trim by hand
610 out of 925 seconds

## Slide 2: Morning - access
09:00 Just as we wanted to move to collisions, beam dump from access system in Pt8 – shielding wall seen open.
  Beam gone, 3 sectors OFF from SIS access interlock.
Investigation by GS – problem was traced to a cable fault inside a LASS rack.
  During the investigations, lost all patrols in Pt8.
  EIS Pt8 seen in bad state during repair  no access possible in the ring.
13:00 New dry test of 90 m un-squeeze. Trip of Q4.R5.
  Have to lengthen the functions a bit more…
14:00 Machine patrolled.
  Many thanks to EN/MEF for help with the patrols !

## Slide 3: Afternoon
15:00 Another access in Pt6 for vacuum (pressure sensor).
Pre-cycle, beam back just before 18:00.
18:00: TCDQ angular alignment.
  Not minimum found for B2 on angle. Decide to remain with ‘0’ angle.
  B1 TCDQ angle -60 urad, compatible with -100 urad found previously. Apply -100 urad angle.
  >> new function needed and test ramp.
22:00 TCDI validation prepared ( tonight).
  Calibration of losses behind collimators.

## Slide 4: Night
23:00 Test ramp and squeeze dumped in ramp – lost S56 & S67, Valves closed, LBDS off due to 400V problem in UA63/67.
  Cause of trip is not understood.
00:40 400 V back, switching on again.
02:00 Problem with TCSGs in Pt6 – lost steps.
  STI piquet could reset.
03:30 Ramp finally starting…
04:00 Beam lost in the squeeze, apparently on TCTs in IR8 – collimator functions?
  Worse than before when the collimator were left in place.

## Slide 5: We can do better..

## Slide 6: Squeeze

## Slide 7
Losses start ~6m (IR1/5), become massive ~3m (IR1/5)

## Slide 8: Early morning
05:40 S78 trip. Cause unclear…
Access needed to restore communication to QPS controller.
Next:
  Collimator setup at 4 TeV (evening)
  Injection protection validation (night)
  Thursday: collisions with nominal bunch – only after squeeze problem is understood (another test with probe).