## Slide 1: MD#2 News & Plan Tue – Wed (19. – 20.6.)
Day | Time | MD | EiC | MP
Tue | 06:00 | 450 GeV  4 TeV: Ramp for chromaticity - missed |  | A
 | 08:00 | Ramp down |  | 
 | 10:00 | 450 GeV: Large Piwinski Angle MD + precycle 2 bunches 2.4e11 – started with 3:30 h delay |  | A
 | 18:00 | 450 GeV  4 TeV: Octupole instability threshold Single full physics beams |  | C
Wed | 02:00 | Ramp down |  | 
 | 04:00 | 450 GeV  4 TeV: Longitudinal dynamics studies |  | B
 | 10:00 | Ramp down |  | 
 | 12:00 | 450 GeV  4 TeV: Beta* leveling 2 nominal bunches |  | C
 | 20:00 | Ramp down |  | 
 | 22:00 | 450 GeV  4 TeV: Long-range beam-beam with high bunch intensity 84b 50 ns 1.7e11 |  | C
Giulia
Ghislain
Alick
Mirko
Ghislain
Alick
Giulia

## Slide 2: MD#2 News & Plan Tue – Wed (19. – 20.6.)
Day | Time | MD | EiC | MP
Tue | 06:00 | 450 GeV  4 TeV: Ramp for chromaticity - missed |  | A
 | 08:00 | Ramp down |  | 
 | 10:00 | 450 GeV: Large Piwinski Angle MD + precycle 2 bunches 2.4e11 – started with 3:30 h delay |  | A
 | 18:00 | 450 GeV  4 TeV: Octupole instability threshold Single full physics beams – successful Ramp for chromaticity |  | C
Wed | 02:00 | Ramp down |  | 
 | 04:00 | 450 GeV  4 TeV: Longitudinal dynamics studies |  | B
 | 10:00 | Ramp down |  | 
 | 12:00 | 450 GeV  4 TeV: Beta* leveling 2 nominal bunches |  | C
 | 20:00 | Ramp down |  | 
 | 22:00 | 450 GeV  4 TeV: Long-range beam-beam with high bunch intensity 84b 50 ns 1.7e11 |  | C
Giulia
Ghislain
Alick
Mirko
Ghislain
Alick
Giulia

## Slide 3
Day | Time | MD | EiC | MP
Thu | 06:00 | Ramp down |  | 
 | 08:00 | 450 GeV  4 TeV: High beta* (1) |  | A
 | 16:00 | Ramp down |  | 
 | 18:00 | 450 GeV: MKI UFO studies |  | C
Fri | 04:00 | 450 GeV  4 TeV: Scraping, diffusion and Repopulation Study and fast losses (with ADT) |  | C+C
 | 12:00 | Ramp down |  | 
 | 14:00 | 450 GeV: Injection and Q20 optics |  | A
 | 22:00 | 450 GeV: RF cavity phase modulation for 25ns |  | B
Draft MD Planning Thu – Fri (21. – 22.6.)
Ghislain
Mirko
Ghislain
Alick
Verena
Mirko

## Slide 4
Day | Time | MD | EiC | MP
Sat | 06:00 | 450 GeV  4 TeV: High beta* (2) |  | A
 | 14:00 | Ramp down |  | 
 | 16:00 | 450 GeV: Transverse Damper studies |  | 
 | 22:00 | Ramp down |  | 
Sun | 00:00 | 450 GeV  4 TeV: Collimation (impedance, nominal settings) |  | C
 | 06:00 | Ramp down |  | 
 | 08:00 | 450 GeV: Beam Instrumentation (BSRT, BGI, wire scan, BPM nonlinearities) |  | A/B/C
 | 16:00 | 450 GeV  4 TeV: Test ramp for emittance calibration |  | B/C
 | 20:00 | Ramp down |  | 
 | 22:00 | 450 GeV: Dynamic Aperture MD |  | D
Mon | 06:00 | Technical Stop |  | 
Draft MD Planning Sat – Mon (23. – 25.6.)
Alick
Mirko
Alick
Enrico
Mirko
Alick
Enrico

## Slide 5
start of 2012 LHC MD block #2

## Slide 6: LPA MD - history
started 3.5 hours late, then 1 h machine set up
~13:45 injected 1 pilot + 2 nominal bunches / beam
ADT off, collision tunes, TCT coarse settings, TDI out, IR angle bumps zeroed (IP 1+5), IR separation collapsed in IPS 1,5 and 8
luminosity signal in LHCb, weak signal (?) in ATLAS, no signal from CMS, dumped
~17:00 injected 1 pilot + 2 bunches of 2.4e11 / beam
clear luminosity signals from LHCb and ATLAS, no signal from CMS, optimized collisions in IPs 1 and 8
reduced spectrometer strength in two steps (-50% and -100%)
ADT work, dump, pre-cycle, spectrometer left at 0

## Slide 7: LPA MD conditions
2.4e11 / bunch; 2 bunches per beam
1st bunch collides in IP 8 only
2nd bunch collides in IPs 1, 5 and 8
injection energy, 1.5 ns bunch length, e~2 mm
ADT off, orbit feedback off,
TCTs at coarse settings, IR angle bumps zeroed in IPs 1 and 5
IP8 crossing angle 4 mrad, 2 mrad, 0 (varied with spectrometer strength)
collision tunes
estimated Piwinski angles ~ 1.1, 0.6, 0
largest Piwinski angle ever!

## Slide 8: LPA MD overview
CMS lumi signal appears at last
ATLAS
lumi
signal
reduced
(steering
effect)
LHCb luminosity signal zero in the database

## Slide 9: LPA MD bunch intensity
X. Buffat
100%
50%
0%
100%
50%
0%
bunch with 3 collisions loses much more intensity;
steepest loss at 50% of LHCb spectrometer strength;
best lifetime at 0 strength
Jose Abelleira, Chandra Bhat, Xavier Buffat, Karel Cornelis, Riccardo De Maria, Rossano Giachino, Mike Lamont, Themis Mastoridis, Alick Mcpherson, Giulia Papotti, Tatiana Pieloni, Ghislain Roy, Belen Salvachua, Daniel Valuch, Frank Zimmermann, + …
qualitatively consistent with expectation

## Slide 10
 | EmitX beam 1 | EmitX beam 2 | EmitY beam 1 | EmitY beam 2
17:00 |  | 1.95+/-0.01 mm (1 collision) 2.07+/-0.01 mm (3 collisions) |  | 2.17+/-0.00 mm (1 collision) 2.56+/-0.02 mm (3 collisions)
17:17 | 2.7+/-0.1 mm (1 collision) 2.10+/-0.03 mm (3 collisions) | 2.0+/-0.1 mm (1 collision) 1.6+/-0.1 mm (3 collisions) | 2.17+/-0.01 mm (1 collision) 1.72+/-0.03 mm (3 collisions) | 2.11+/-0.01 mm (1 collision) 1.64+/-0.01 mm (3 collisions)
17:35 | 2.53+/-0.01 mm (1 collision) 2.0+/-0.1 mm (3 collisions) | 2.01+/-0.01 mm (1 collision) 1.56+/-0.02 mm (3 collisions) | 2.11+/-0.04 mm (1 collision) 1.67+/-0.02 mm (3 collisions) | 2.07+/-0.05 mm (1 collision) 1.53+/-0.08 mm (3 collisions)
LPA MD bunch emittance
bunch with 3 collisions shrinks

## Slide 11
fill with beam 2
decreasing octupoles' current from ~ 450 A to 97 A (on flat-top before the squeeze) where beam losses appeared and then the beam was dumped
estimated Q’ + 5 units (trim of 3 units on top of the ~ 1-2 assumed to be in physics)
octupole instability threshold at 4 TeV
Elias Metral, Alexey Burov, Nicholas Mounet, Giulia Papotti
consistent with impedance model
to be repeated for squeezed optics

## Slide 12
chromaticity at flat top
Giulia Papotti,
Nicolas Mounet,
Alexey Burov,
et al

## Slide 13
chromaticity varies with octupole strength
Giulia Papotti, Nicolas Mounet, Alexey Burov, et al

## Slide 14
Summary of chromaticity measurement: At flat top with 450 A in the octupoles, chromaticity around 1 in horizontal, 2 in vertical (both beams). Trimming down the octupoles has a large effect on chromaticity: +4/+5 units in horizontal, -1/-2 in vertical. With zero A in the octupoles losses were observed (due to an instability ? chromaticity possibly negative in vertical and transverse feedback was off). Chromaticity was also measured during squeeze (B1 essentially, as B2 tune got very noisy at the end of the squeeze): Q'~1 in horizontal, ~2 in vertical. Reducing octupoles shows the same trends as before squeeze. Fast losses were observed in the end, probably partly due to the opening of the phase loop on B2 (too low intensity).
Giulia Papotti, Nicolas Mounet, Alexey Burov, et al

## Slide 15
longitudinal dynamics studies
Injected 8 “indivs” with different intensities but similar bunch lengths, longitudinal measurements being taken with phase loop off (was on for injecting).
E. Shaposhnikova,
J. Esteban Muller,
R. Calaga et al
lost 1 h due to
IT upgrade
at 6:30
synchronous
phase,
synchrotron
frequency,
tune shift , etc.
for different
intensity
and bunch length