## Slide 1: 13.12.2009
-09:00: Prepared new fill
B1: QX=0.293, QY=0.269; lifetime = 25h ✔ B2: QX=0.297, QY=0.267; lifetime = 5h ✗
Strong 50Hz and 100hz lines on Beam1 spectrum
-13:00: Terminated fill: Beam2 intensity dropped to 1/3rd (7 1010  2.5 1010)
-13:30: Prepared new fill but tried to inject Beam2 first
 accidentally took out beam with last Beam1 injection ✗
-14:00: New stable beams with correct tune values: lifetimes 25h and 5h
Transverse IP scans for CMS, LHCb and ALICE ✔
-18:30: Terminate fill when Beam2 intensity dropped to 1/3rd
 Try wire scanner with ‘stable beam mode’ on (CMS informed) ✔
 Analyzed b-beat measurement at IPs  no preference for a beat ✗
 Try tune adjustment (DQ 10-2 with ‘stable beam mode’ off) ✔

## Slide 2: 13.12.2009: First fill tunes
Strong 50Hz lines in horizontal and 100 Hz lines in vertical tune of Beam1.
Not visible in Beam2. These are not synchrotron lines
(frev = 11.2455 kHz, fsync = 63.6 Hz according to RF parameters)
Beam1: Beam2:

## Slide 3: 13.12.2009: Transverse IP scans
CMS: LHCb:

## Slide 4: 13.12.2009: Parasitic Wire Scans
Beam2 horizontal: Beam2 vertical
Comparing beam size from wire with synchrotron light monitor
Wire: sx = 0.98mm sy = 3.0mm BSRT: sx = 1.10mm, sy = 2.7mm  ca factor 2 between sy and sx

## Slide 5: 13.12.2009: Parasitic Wire Scans
Beam1 horizontal: Beam1 vertical
Comparing horizontal and vertical beam size from wire measurements:
Wire: sx = 0.82mm, sy = 1.5mm  also factor 2 between sy and sx
Have not yet measurement at beginning of fill.  not yet possible to conclude
or exclude blow up for Beam1

## Slide 6: 13.12.2009: Measured b-functions at IPs
IP | Beam1 bx [m] | Beam1 by [m] | Beam2 bx [m] | Beam2 by [m] | nominal [m] | Ratio sx | Ratio sy
1 | 12.7 ± 2.5 | 13 ± 1 | 9 ± 1.5 | 16 ± 0.5 | 11 / 11 | 1.2 | 0.9
2 | 8.3 ± 0.1 | 8.8 ± 0.5 | 12 ± 1.5 | 13 ± 20 | 10 / 10 | 0.83 | 0.82
5 | 16 ± 0.5 | 12.7 ± 1 | 13 ± 1 | 9.6 ± 1.5 | 11 / 11 | 1.1 | 1.15
8 | 11.3 ± 19 | 12.3 ± 2 | 9.5 ± 2.5 | 7.8 ± 0.5 | 10 / 10 | 1.1 | 1.25

## Slide 7: 13.12.2009: Tune Adjustments for Beam2
B1: Qx = 0.293, Qy = 0.269; lifetime = 26h B2: Qx = 0.297, Qy = 0.267; lifetime = 5h
B1: Qx = 0.293, Qy = 0.269; lifetime = 25h B2: Qx = 0.312, Qy = 0.305; lifetime = 12h ✔
1/11
1/7
1/10
1/3

## Slide 8: 13.12.2009: New Tunes for Beam2
B2: QX=0.312, QY=0.305; lifetime = 12h ✔

## Slide 9: 13.12.2009
-19:00: Dumped Beam1 before Beam2  no effect on Beam2 lifetime
-19:30: New fill new tunes for Beam2:
B1: Qx = 0.291, Qy =0.268; lifetime ≈ 10 h B2: Qx = 0.311, Qy =0.305; lifetime ≈ 10 h
-22:50: Beam lost due to cryo problem in S12
Cold compressor off in sector 12
estimated time for recovery: 12 hours  10am Sunday
 access ALICE
 RQ6.L6B1/2 tripped during switch on to STANDBY
-07:00: Cryo conditions OK preparing pre-cycle for S12
 problems related to QPS

## Slide 10: 13.12.2009: Last 24 hours - currents

## Slide 11: 13.12.2009: Last 24 hours – light monitor
Horizontal beam size for Beam1 seems to shrink at beginning of fill (1st hour)
 scraping at collimators? Consistent with low lifetime at start of fill (ca. 1h)

## Slide 12: 13.12.2009: Last 2 Fills Lifetimes
Lifetimes consistently bad (ca. 1h) for first hour of fills

## Slide 13: 13.12.2009: Plan for the weekend:
-Finish luminosity production at 450 GeV: 16 on 16 bunches?
-Tune adjustments Beam1?
-Turn separation bumps on IP by IP and look for effect on beam lifetime
-Inject with separation bumps on?
-Chromaticity adjustments and knob commissioning (end of fill)
-Orbit bumps at synchrotron light monitor (end of fill)
-fill with high intensity
-test b* knobs
-Ramp test: Orbit correction at end of ramp and optics verification
-MPS and beam dumping system at 1.1 TeV (end of ramp?)
-Protection devices and collimation system setup at 1.1 TeV
-intermediate energy dumps
-abort gap cleaner commissioning

## Slide 14: 13.12.2009: Plan for the weekend:
-bumps at TOTEM Roman Pots
-ATLAS aperture H re-check
Other miscellaneous work:
      -finish circuit polarity checks
      -finish kick response measurements
      -orbit feedback commissioning
      -nQPS quench threshold test with beam (bunch intensity < 2 109)

## Slide 15: 13.12.2009: First fill tunes
1/11
1/7
1/10
1/3
B1: QX=0.293, QY=0.269; lifetime = 25h B2: QX=0.315, QY=0.310; lifetime = ??h
B1: QX=0.315, QY=0.310; lifetime = ??h B2: QX=0.315, QY=0.310; lifetime = ??h